## Slide 1
INTERNSHIP REPORT
Robotics Error Detection &
Sensor Monitoring
In the Body Shop for MQ4i Vehicle Production at KIA India
Muthirevula Tharun Reddy
Roll No: 24691A32S8
B.Tech — CSE (Data Science)
Madanapalle Institute of Technology & Science
KIA INDIA PRIVATE LIMITED • BODY SHOP DEPARTMENT • 2026

## Slide 2
02
Internship at a Glance
KIA India Private Limited — Body Shop Department
300K+
Annual vehicle production capacity at the Anantapur plant
40
Days on-site in the Body Shop (May 21 – Jun 29, 2026)
1
New model supported: the upcoming MQ4i
10+
Robotic fault types observed & diagnosed on the line

## Slide 3
03
Internship Objectives
What the placement in the Body Shop was designed to achieve
01
Understand the complete Body Shop production process end to end
02
Observe robotic welding and automated body-assembly operations
03
Monitor Zig sensors and conveyor systems in real time
04
Identify robotic faults and sensor-related production errors
05
Assist engineers in troubleshooting live production issues
06
Learn safety procedures for working around industrial robots

## Slide 4
04
Body Shop Production Flow
From stamped panels to a finished, painted vehicle body
Press Shop
▶
Body Assembly
▶
Anticorrosion
▶
Priming
▶
Finishing
▶
Assembling
Body Assembly is the internship's focus area — robots here perform spot welding, joining
and dimensional verification before the body moves on to corrosion protection and paint.
Zig sensors + PLC controllers confirm correct body position at every station before a robot is allowed to weld.

## Slide 5
05
Core Technologies on the Line
The four systems that keep robotic welding synchronized
Z
Zig Sensors
Detect vehicle-body arrival & correct positioning at each workstation before welding starts
P
PLC Controllers
Process sensor signals, coordinate robots and conveyors, and halt production on any fault
H
HMI Displays
Give operators real-time status, error messages, and manual restart controls
C
Conveyor System
Moves the body between robotic stations automatically once each stage completes

## Slide 6
06
Common Robotic Errors Observed
Recurring faults tracked on the MQ4i welding line
Zig sensor detection failure
Robot waiting for sensor signal
Conveyor synchronization error
Robot communication failure
Emergency stop activation
Body misalignment
PLC communication delay
Robot position error
Safety gate interlock activation
Welding cycle interruption

## Slide 7
07
Error Detection & Troubleshooting
The five-step response engineers followed on every fault
1
HMI Alert
Error message appears on the HMI screen
2
Identify
Locate the affected robot or sensor
3
Verify
Check sensor signals & conveyor movement
4
Correct
Adjust sensor, reset PLC, or reset robot
5
Resume
Trial run, then restart full production

## Slide 8
08
Results & Benefits Observed
What accurate sensing and fast troubleshooting delivered on the line
Production Efficiency
Continuous production, minimal interruptions
Better robot–sensor coordination
Increased manufacturing speed
Robotic Downtime
Faster fault identification & troubleshooting
Reduced production delays
Better equipment utilization
Sensor Accuracy
Accurate body positioning every cycle
Fewer welding defects
Reliable, safer automation

## Slide 9
09
Skills Gained
Bridging classroom learning with real industrial practice
Technical Skills
Industrial robotics & automation
Zig sensor monitoring
PLC & HMI fundamentals
Conveyor automation
Robotic fault identification
Preventive maintenance concepts
Professional Skills
Teamwork on the shop floor
Communication with engineers
Problem-solving under pressure
Analytical observation
Time management
Workplace safety discipline

## Slide 10
Conclusion & Future Scope
Where robotics & Industry 4.0 in the Body Shop are headed next
This internship built practical understanding of how robots, Zig sensors, PLCs, HMIs and conveyors work together to deliver precise, uninterrupted MQ4i body production — and sharpened my interest in intelligent manufacturing.
AI-assisted robotic decision-making
Smart vision-based inspection
Predictive maintenance via IoT
Digital twin technology
Collaborative robots (cobots)
Cloud-connected smart factories
Muthirevula Tharun Reddy | 24691A32S8 | MITS, Madanapalle